## Slide 1: Nationally designated areas
Reporting 2026 | Spatial data
Christopher Philipsen | ETC DI

## Slide 2
Spatial data requirements largely unchanged
Minor adaptations following INSPIRE developments
Revision
  Addition of new field “thematicId” → contains the site code information, which is also the natDAId in the descriptive part (Type 2)
  INSPIRE version 4 and 5 datasets accepted as input besides independent shapefile → .shp and .gml accepted as file formats
  Harvest/Import from Service discontinued because of non-use
Spatial data - Revision
Nationally designated areas
Reporting 2026 | Spatial data

## Slide 3
Spatial data input can be derived both from INSPIRE Protected Sites (PS) and INSPIRE Area Management (AM) → common elements will be used or can be extracted in case Shapefile is generated
Mapping of elements between INSPIRE specifications and shapefile stays largely unchanged
Spatial data - Revision
Nationally designated areas
Reporting 2026 | Spatial data

## Slide 4
Spatial data – Mapping INSPIRE to Shapefile
Nationally designated areas
Reporting 2026 | Spatial data

## Slide 5
Nationally designated areas
Reporting 2026 | Spatial data
INSPIRE services data
Shapefile structure

## Slide 6
Geometry: point or (multi-)polygon representation of the designated area
inspireId: object identifier of the designated area
  localId: unique identifier within the namespace → proposed to reuse the nationalId where localId not defined
  namespace: namespace uniquely identifying source → proposed to use “EIONET.ENVIRONMENT.PS.NATDA.countrycode”
  versionId: in case the area has been mapped multiple times versioning can be applied → optional
Spatial data - Structure
Nationally designated areas
Reporting 2026 | Spatial data
Each area can only be included once in the spatial data since the spatial data can only contain valid representations

## Slide 7
legalFoundationDate: date the real-world area was established by legal process → format: YYYY-MM-DDThh:mm:ssZ (INSPIRE PS v4) (e.g., 1987-01-01T01:01:01Z) → format change with INSPIRE v5: YYYY-MM-DD (e.g., 1987-01-01) → both formats are accepted but for NatDA only YYYY is used
siteName: Name of the designated area → for countries with non-Latin characters reporting by Shapefile format: remember to provide the .cpg file to ensure correct encoding
thematicId: thematic identifier within the schema → site code / natDAId of area under normal circumstances
Spatial data - Structure
Nationally designated areas
Reporting 2026 | Spatial data

## Slide 9
Thank you!